## Slide 1: CS143 Week#3 (Disk)
Jia (Jason) Teoh
slides courtesy of Ariyam Das
Notes: We did cover indexes in class on Wednesday, but those are a bit more in-depth so we’ll cover them in detail next week. If interested we can go through an overview of sparse vs dense today (ISAM/B+ next week though)

## Slide 2: Announcements
Discussion 2B (2-3:50) cancelled.
  Feel free to attend any of the other two discussions.
Project 2B released
  Due Monday October 30th @ 11PM on CCLE
  Post questions on Piazza
Notes: Um... I guess hw 2 was also due right at the moment Jason teaches his discussion. so not exactly worthwhile to mention that...
all slides uploaded to CCLE later.
also, everybody has signed up on Piazza right? RIGHT?! yay.
(does anybody else actually read these notes?)

## Slide 3: SQL - Cubes and Rollups
FYI
https://technet.microsoft.com/en-us/library/ms189305(v=sql.90).aspx

## Slide 4: SQL Authorization
See handout (w3_1.pdf)

## Slide 7: A typical disk
2 platters
2 surfaces/platter
5000 tracks/surface
1000 sectors/track
1KB/sector
6,000 RPM (rotational speed)

## Slide 8: Overall Capacity
Q: 2 platters, 2 surfaces/platter, 5000 tracks/surface, 1000 sectors/track, 1KB/sector. What is the overall capacity?
2 platters * 2 surfaces/platter * 5000 tracks/surface * 1000 sectors/track * 1KB/sector = 20 * 1000 * 1000 KB = 20 GB
Notes: easy – just multiply them all together

## Slide 9: Access Time
Access time =
(seek time) + (rotational delay) + (transfer time)

## Slide 10: Seek Time
Seek time: time to find the target track
  Typical average seek time: 10 ms
Notes: for any hw/test questions we’ll give you the information needed to calculate though.

## Slide 11: Rotational Delay
Rotational delay: time to rotate to the target sector
  For 6000 RPM, average rotational delay=0.5*(1min/6000)=0.5*60sec/6000=5 ms
Head Here
Block I Want
Notes: Why 0.5? we’re assuming random access on the disk, so on average it’ll end up halfway around the disk (thus you need half a rotation)

## Slide 12: Transfer Time/ Rate
Time to read one block
  Read a track, rotate a circle: 1min/6000 = 10 ms/track
  Read one sector(block): (10ms/track) / (1000sector/track) = 0.01ms/sector
Transfer rate: 1KB/(0.01ms/sector)=100MB/s
Disk Head
Read blocks as
the platter rotates
[6000 RPM, 1000 sector/track, 1KB/sector]
Notes: reading the whole track = RPM
sector (aka block) is a fraction of the track
transfer rate: read time for a block combined with the data in a block

## Slide 13: Sequential Access
Time to read 3 sequential blocks
  seek time: 10 ms
  rotational delay: 5 ms
  transfer time: 0.01ms
  Access time:
    10ms+5ms+3*(0.01ms)= 15.03ms

## Slide 14: Random Access
Time to read 3 random blocks
  seek time: 10 ms
  rotational delay: 5 ms
  transfer time: 0.01ms
  Access time:
    (10ms+5ms+0.01ms)*3=45.03ms
Very expensive, avoid random I/O as much as we can

## Slide 15: Answer query: Full Search v/s Index
SELECT * FROM Student WHERE sid = 40
sid | name | GPA
20 | Elaine | 3.2
70 | Peter | 2.6
40 | Susan | 3.7
Notes: That’s all I have for slides right now. Is there other stuff you guys want to cover?
Optional adhoc review: sparse vs dense index
dense: entry for every single record
sparse: entry for head of every block (really only makes sense if blocks are sequential)
multi-level index: used so highest level index can still be stored in memory, reduce page loads for lookup
first-level (lowest/closest to data blocks) must be dense if used in a secondary index, since the data isn’t clustered (ie sequential keys might point to opposite ends of the table)